## Slide 1: A fast AI surrogate for offshore wind monopiles under waves and earthquakes
Two-semester plan: work, expected results, technologies and methods
Notes: Project in one line: train an AI model on many computer simulations so it can predict, in under a second, how the seabed and a monopile respond when waves and an earthquake hit together.

## Slide 2: Why this matters: combined loads weaken the seabed
Waves
Thousands of slow pushes in a storm raise pore-water pressure around the pile.
Earthquake
20–40 s of strong shaking can push the already-weakened sand towards liquefaction.
Simulation is slow
One realistic finite element run takes hours; risk checks need thousands of scenarios.
Our idea
Run the slow simulator about 1,000 times, once.
Train a Fourier Neural Operator (FNO) to copy it.
Add a physics check (balance laws) to the training loss.
Predict pore pressure and pile tilt in under 1 second.
Research question: does the physics check reduce error when training data is scarce?
Notes: Waves raise pore pressure before the earthquake arrives, which is why the combination is dangerous. FE tools like OpenSees are accurate but slow, so we build a surrogate.

## Slide 3: Methodology: from simulations to a sub-second model
1. Generate loads
Scaled earthquake records + random sea states
2. Simulate
2D OpenSees soil–pile model, nonlinear sand
3. Build dataset
~1,000 runs on a regular grid, held-out quakes
4. Train FNO
Load histories → pore-pressure field + tilt
5. Predict
New scenario answered in under 1 second
Physics-informed loss (the PINN part)
Loss = data error + λ × balance-law residual. Only force balance and water mass balance are enforced, since our sand is nonlinear.
How we check it
Test on earthquakes never seen in training, compare against an LSTM baseline, and report errors on engineering numbers.
Notes: Steps 1–3 are simulation work, steps 4–5 machine learning. The physics loss only enforces laws our nonlinear soil actually obeys.

## Slide 4: Timeline: simulation first, machine learning second
Sem 1 · Oct 7–Nov 10
Break
Semester 2 · ~16 weeks
Scope, reading, tool warm-up
Soil column + benchmark
Load generator
Mini-surrogate (soil column)
Sem 1 report + review
2D pile model + pilot runs
Full dataset (~1,000 runs)
Baseline tilt model
Full-field FNO
Physics loss experiment
Evaluation + demo
Thesis + paper draft
Simulation and data
Machine learning
Reading, writing, reviews
Notes: Semester 1 ends on Nov 10, 2026, so it is compressed to 5 weeks. The 2D pile model moves into the break; Semester 2 opens with the full dataset. Break length assumed at about 4 weeks.

## Slide 5: Semester 1 results: a working mini-version of the project
5
weeks, Oct 7 to Nov 10, 2026
Safety net: these four results stand on their own even before the pile model exists.
Approved scope note
Two-page note with the exact novelty claim, signed off by the guide.
Checked soil model
Pore-pressure curves plotted next to the published benchmark.
Load generator
One function call returns any number of combined wave + earthquake histories.
Mini-surrogate
FNO vs LSTM error on unseen earthquakes, and the measured speed-up over OpenSees.
Notes: End of Semester 1 presentation: problem and gap, checked soil model, mini-surrogate results, load generator examples, and the pile model plan for the break.

## Slide 6: Technologies and methodologies
Technologies
Simulation
OpenSeesPy (u-p elements)
Earthquakes
PEER NGA-West2
Waves
Python: JONSWAP + Morison
Sampling
SciPy Latin hypercube
Data
HDF5 (h5py)
ML
PyTorch + neuraloperator
Compute
College HPC; Kaggle / Colab
Plots, code
Matplotlib, ParaView, Git
Methodologies
Finite elements: 2D plane-strain u-p (Biot) formulation with a nonlinear sand model (PDMY02 or PM4Sand).
Loading: scaled earthquake records plus random sea states, joined with a random time gap.
Design of experiments: Latin hypercube sampling of soil and load parameters.
Operator learning: Fourier Neural Operator; LSTM as the baseline.
Physics-informed loss: force and water mass balance via finite differences.
Validation: held-out earthquakes, engineering error metrics, out-of-range tests.
Notes: Everything is free or open source. The free Kaggle tier is enough for both simulations (4 CPU cores, background sessions) and FNO training if HPC is unavailable.